## Slide 1
Level 0 | 
Module | ChargeGuard Pro+
Inputs | Power 12V, Lithium-ion Button, Alkaline button, reset button, Temperature sensor
Output | AA Alkaline battery, Lithium-ion button cell (2032 or 2025) , 12V Fan, LCD indicator
Functionality | Uses 12V power source to charge either a lithium-ion button cell or Alkaline AA batteries. Should include an LCD indicator to display temperature.
Power 12V
Reset Button
Fan
Level 0
LCD indicator
ChargeGuard Pro+
Lithium-ion button cell (2032/2025)
Lithium-Ion charge Button
Alkaline Button
Temperature sensor
AA Alkaline battery

## Slide 2
Huzzah_ESP32 Module
Power (12V)
Reset
Start/Stop Switch (AA)
Voltage Regulator (5V out)
Temperature Sensor
OLED Screen
Start/Stop Switch (BC)
Voltage (AA)
Voltage (BC)
AA Voltage Divider
BC Voltage Divider
Battery Temp
BC Charge module
AA Charge module
Solenoid
User Feedback
Eject AA battery
Battery Charge
Battery Charge
Level 1 - ChargeGuard Pro+
Current AA Voltage
Current BC Voltage
5VDC
SDA/SCL Signal
GPIO Charge Start Signal
GPIO Charge Start Signal
GPIO Battery Eject Signal
SDA/SCL Signal

## Slide 3
AA Voltage Divider
AA Voltage Divider: Level 1
Level 1 | 
Module | AA Voltage Divider
Inputs | AA Battey Voltage
Output | AA Battery Voltage
Functionality | Use a voltage divider to measure current value of AA battery voltage
Voltage (AA)
Voltage (AA) ADC (to Huzzah_ESP32)

## Slide 4
BC Voltage Divider
BC Voltage Divider: Level 1
Level 1 | 
Module | BC Voltage Divider
Inputs | BC Battey Voltage
Output | BC Battery Voltage
Functionality | Use a voltage divider to measure current value of BC battery voltage
Voltage (BC)
Voltage (BC) (to Huzzah_ESP32

## Slide 5
Temperature Sensor
Temperature Sensor: Level 1
Level 1 | 
Module | Temperature Sensor
Inputs | 5VDC (power supply), Battery Temperature measured in °C
Output | SDA/SCL to the Huzzah_ESP32
Functionality | Measure temperature of battery that is currently being charged, read using the ESP32 I2C bus
5VDC
SDA (to Huzzah_ESP32)
SCL (to Huzzah_ESP32)
Battery Temperature (°C)

## Slide 6
OLED Screen
OLED Screen: Level 1
Level 1 | 
Module | OLED Screen
Inputs | 5VDC (power supply), SDA/SCL from the Huzzah_ESP32
Output | Battery temperature, battery voltage
Functionality | Display current system information to user via OLED Screen
5VDC
SDA (from Huzzah_ESP32)
SDL (from Huzzah_ESP32)
Battery Temperature
Battery Voltage
Current System State

## Slide 7
Solenoid
Solenoid: Level 1
Level 1 | 
Module | Solenoid
Inputs | 5VDC
Output | Actuating Armature
Functionality | When the battery is done charging, using the armature to eject the charged battery
GPIO Start Signal
Actuating Armature
5VDC

## Slide 8
Huzzah_ESP32
Huzzah_ESP32: Level 1
Level 1 | 
Module | Huzzah_ESP32
Inputs | Start/Stop Charge Button (Qty. (1) for each AA and BC batteries), BC/AA Current Voltage, SDA/SCL from temp sensor, Reset, 5VDC from regulator to power uC
Output | Solenoid start/stop signal, BC and AA charge module Start/Stop charging signal, SDA/SCL to user OLED display
Functionality | Continuously read and store current values for temperature, voltage, and button states. Send signals to start/stop charging based on input thresholds and system state. Display real-time system status: temperature, voltage, charging state, and errors. Transition between states (e.g., charging, waiting, error) based on input conditions and thresholds.
5 VDC
SDA/SCL From Temp Sensor
Start/Stop Button (BC)
RESET
AA Battery Voltage
BC Battery Voltage
Start/Stop Button (AA)
SDA/SDL to OLED
AA Charge Module Start/Stop Signal
BC Charge Module Start/Stop Signal
Solenoid Start/Stop Signal

## Slide 9
Voltage Regulator
Voltage Regulator : Level 1
Level 1 | 
Module | Voltage Regulator
Inputs | 12 VDC (from 12VDC wall wart)
Output | 5 VDC
Functionality | Steps down 12VDC input to a stable 5VDC output.
12 VDC
5 VDC

## Slide 10
AA Charge Module
AA Charge Module: Level 1
Level 1 | 
Module | AA Charging Module
Inputs | Start Charging Signal
Output | (1.3 – 1.6) VDC Charging Voltage
Functionality | Starts charging AA battery when a start signal comes from the Huzzah_ESP32
GPIO Pin Start Signal (From Huzzah_ESP32
(1.3 – 1.6) VDC

## Slide 11
BC Charge Module
BC Charge Module: Level 1
Level 1 | 
Module | BC Charging Module
Inputs | Start Charging Signal
Output | 4.2 VDC Charging Voltage
Functionality | Starts charging BC battery when a start signal comes from the Huzzah_ESP32
GPIO Pin Start Signal (From Huzzah_ESP32
4.2 VDC